*********DRAFT*********
Adapting the ICOBOARD ZIPCPU
to the CATBOARD
06/02/18
*********DRAFT*********

ICOBOARD RPi

RPI_SPI_CLK H11 Pin 23 Pi icoboard

rpi_cs D4 IOT_224 Pin 26 Pi icoboard

CATBOARD RPi

CATBOARD connection to FPGA pins PMOD 2 & PMOD 3 push button switches, dip switch, and leds.

CATBOARD sw1 & sw2

CATBOARD leds

BCM11_SCLK Pin 23 CATBOARD

BCM7_CE1 Pin 26 CATBOARD

2.)	The 2nd issue is the PMOD connections to FPGA are different.
3.)	Third, I do not have a Diglient PMOD 4 push button switch module.
4.)	The 4th issue is the PHASE LOCK LOOP difference.
Post on #yosys
Pin C8 is my USER_CLK comes from a 100MHz osc. It is connected to IOT_197_GBIN1 on HX8K. When I try using it for as an input to PLL I get the fatal error: bad constraint on `i_clk': no PLL at pin C8.
Can only certain pins be used as inputs to PLL?
daveshah
develonepi3: use the SB_PLL40_CORE instead of SB_PLL40_PAD variant (and REFERENCECLK in instead of PACKAGEPIN)
set_io clk_100mhz C8 #R9

set_io pmod1_1 A11 #D8
set_io pmod1_2 B12 #B9
set_io pmod1_3 B14 #B10
set_io pmod1_4 B15 #B11
# 654321 catboard # 654321 icoboard
# xxxxxx PMOD3 A # xxxxxx PMOD1 A
# xxxxxx PMOD3 B # xxxxxx PMOD1 B
# 654321 # 654321
#
set_io pmod1_7 B10 #B8
set_io pmod1_8 B11 #A9
set_io pmod1_9 B13 #A10
set_io pmod1_10 A15 #A11

CATBOARD connection to FPGA pins PMOD 2 & PMOD 3 push button switches, dip switch, and leds.

In top.v

module top(clk_100mhz, pmod1_1, pmod1_2, pmod1_3, pmod1_4, pmod1_7, pmod1_8,
  pmod1_9, pmod1_10, pmod2_7, pmod2_8, pmod2_9, pmod2_10, rpi_sck, rpi_cs,
  rpi_mosi);

input rpi_sck, rpi_cs, rpi_mosi;
rpi_sck
rpi_cs
rpi_mosi

spi_ram_slave spi_ram_slave(clk, rpi_sck, rpi_cs, rpi_mosi,
  ram_addr, ram_data, ram_wr);
module spi_ram_slave(clk, sck, cs, mosi, ram_addr, ram_data, ram_wr);
PMOD pin out on icoboard

“lrwxrwxrwx 1 root staff 34 May 18 20:10 /usr/local/bin/config_cat -> /home/pi/catboard_yosys/config_cat”

#!/bin/bash

# A script to configure Lattice iCE40 FPGA by SPI from Raspberry Pi
#
# Copyright (C) 2015 Jan Marjanovic <jan@marjanovic.pro>
#
# This program is free software: you can redistribute it and/or modify
# it under the terms of the GNU General Public License as published by
# the Free Software Foundation, either version 3 of the License, or
# (at your option) any later version.
#
# This program is distributed in the hope that it will be useful,
# but WITHOUT ANY WARRANTY; without even the implied warranty of
# MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
# GNU General Public License for more details.
#
# You should have received a copy of the GNU General Public License
# along with this program. If not, see <http://www.gnu.org/licenses/>.

echo ""
if [ $# -ne 1 ]; then
    echo "Usage: $0 FPGA-bin-file "
    exit 1
fi

if [ $EUID -ne 0 ]; then
    echo "This script must be run as root" 1>&2
    exit 1
fi

if [ ! -d /sys/class/gpio/gpio25 ]; then
    echo "GPIO 25 not exported, trying to export..."
    echo 25 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio25 ]; then
echo "ERROR: directory /sys/class/gpio/gpio25 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 25 exported"
fi

if [ ! -d /sys/class/gpio/gpio17 ]; then
    echo "GPIO 17 not exported, trying to export..."
    echo 17 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio17 ]; then
echo "ERROR: directory /sys/class/gpio/gpio17 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 17 exported"
fi

if [ ! -d /sys/class/gpio/gpio22 ]; then
    echo "GPIO 22 not exported, trying to export..."
    echo 22 > /sys/class/gpio/export
    if [ ! -d /sys/class/gpio/gpio22 ]; then
echo "ERROR: directory /sys/class/gpio/gpio22 does not exist"
exit 1
    fi
else
    echo "OK: GPIO 22 exported"
fi

echo ""
if [ -e /dev/spidev0.0 ]; then
    echo "OK: SPI driver loaded"
else
    echo "spidev does not exist"

    lsmod | grep spi_bcm2708 >& /dev/null

    if [ $? -ne 0 ]; then
echo "SPI driver not loaded, try to load it..."
modprobe spi_bcm2708

if [ $? -eq 0 ]; then
   echo "OK: SPI driver loaded"
else
   echo "Could not load SPI driver"
   exit 1
fi
    fi
fi

echo ""
echo "Setting GPIO directions"
echo out > /sys/class/gpio/gpio25/direction
cat /sys/class/gpio/gpio25/direction
echo out > /sys/class/gpio/gpio22/direction
cat /sys/class/gpio/gpio22/direction
echo in > /sys/class/gpio/gpio17/direction
cat /sys/class/gpio/gpio17/direction

echo "Setting output to low"
echo 0 > /sys/class/gpio/gpio25/value
cat /sys/class/gpio/gpio25/value

#echo ""
#echo "Please reset the iCE40 FPGA board"
#echo "Press any key..."
#read

echo "Reseting FPGA"
echo 0 > /sys/class/gpio/gpio22/value
cat /sys/class/gpio/gpio22/value
echo 1 > /sys/class/gpio/gpio22/value
cat /sys/class/gpio/gpio22/value

echo "Checking DONE pin"
cat /sys/class/gpio/gpio17/value

echo "Continuing with configuration procedure"
dd if=$1 of=/dev/spidev0.0

echo -e "\x0\x0\x0\x0\x0\x0\x0" > /dev/spidev0.0

echo "Setting output to high"
echo 1 > /sys/class/gpio/gpio25/value
cat /sys/class/gpio/gpio25/value

echo "Checking DONE pin"
cat /sys/class/gpio/gpio17/value

“cd otl-icoboard-pmodoledrgb-demo/stream-tool/”

“ffmpeg -f v4l2 -i /dev/video0 -s 96x64 -f rawvideo -pix_fmt rgb565 - | ./stream-tool”